## Slide 2: Eucalyptus Networking
Eucalyptus Education Services Revision C

## Slide 3: Module Topics
Four Eucalyptus network modes
IP addresses
  Eucalyptus host IP addresses
  Instance public IP addresses
  Instance private IP addresses
Instance Network Security
  Layer 3 IP firewalls
  Layer 2 VLANs
The eucalyptus.conf file

## Slide 4: Network Modes
Eucalyptus supports four network modes
  SYSTEM (default)
  STATIC
  MANAGED
  MANAGED-NOVLAN
Configured in /etc/eucalyptus/eucalyptus.conf
  On Cluster Controller and Node Controller (VNET_MODE)
Choice depends on two factors:
  Eucalyptus features you require or desire
    Security groups, elastic IP addresses, VLAN network isolation
  Level of control over the underlying physical network
Notes: Eucalyptus installation defaults to SYSTEM network mode. Edits must be made to the /etc/eucalyptus/eucalyptus.conf file in order to change to another network mode.
SYSTEM and STATIC network modes are very similar. The primary difference between them is where the DHCP server is implemented.
MANAGED and MANAGED-NOVLAN network modes are very similar. The primary difference between them is support for launching instances in different virtual LANs (VLANs).
Which network mode you choose depends on two factors: The features you want and the degree of control you have over the underlying network.
Most of the rest of this module discusses these modes in much more detail.

## Slide 5: SYSTEM – Characteristics and Features
DHCP Server | External to Eucalyptus
Elastic IP Addresses1 | Not available
Security Groups2 | Not available
VM Layer 2 Isolation | Not available
1 IP addresses manually reserved and assigned to virtual machines
2 A set of firewall rules applied to a set of virtual machines
Notes: The characteristics and features of SYSTEM network mode.

## Slide 6: SYSTEM – Logical View
Walrus
storage
Cloud
Controller
Cluster
Controller
Storage
Controller
corporate LAN
corporate
DHCP
server
VM
VM
VM
Br
Node
Controller
Node
Controller
Node
Controller
Node
Controller
Notes: Here is what it looks like logically. Note that Eucalyptus is not providing or configuring the DHCP controller.

## Slide 7: SYSTEM Network Mode
The least intrusive network mode.
Instance receives a single IP address from the organization’s DHCP server.
All instances have direct network access through the network bridge in the Node Controller.
  Instances appear as physical machines on the network.
It’s IT administration’s responsibility to manage any security (firewalls) or network address translation.
Seldom used in production environments.
Notes: Least intrusive networking mode because it requires no substantial changes to the existing network infrastructure.
The DHCP server for the virtual machines must be provided by a DHCP server external to Eucalyptus. Each virtual machine receives a single IP address from the DHCP server. Each virtual machine will use this IP address for not only communication to nodes external to the cloud, but also to other virtual machines within the cloud.
A bridge must be created on the Node Controllers for Eucalyptus to use. All virtual machines have direct network access using the virtual bridge created by the hypervisor in the Node Controller. There are no virtual subnets—instances appear on the physical network as if they were physical machines.
It is up to IT management to manage any network security firewalls or network address translation that might be required by the organization.

## Slide 8: SYSTEM – Physical Example
DHCP server
company network
173.205.188.130 eth0
173.205.188.131 eth0
173.205.188.132 eth0
front-end (CLC Walrus CC SC)
Node Controller
Node Controller
Notes: This is an example of a simple configuration. The front-end host, the Node Controller hosts, and the instances are all on the 173.205.188.0 network.

## Slide 9: SYSTEM Network Mode Requirements
Must have a pre-existing DHCP server on the network.
  Configured to supply instances with IP addresses
A range of IP addresses must be available for use by Eucalyptus hosts and instances.
The Ethernet interface on the Node Controller must be configured with a bridge.
  The DHCP server must be reachable from the bridge.
Notes: If the Node Controller has more than one Ethernet interface, the interface that communicates with the Cluster Controller must be configured with a bridge.

## Slide 10: STATIC – Characteristics and Features
DHCP Server | Cluster Controller
Elastic IP Addresses | Not available
Security Groups | Not available
VM Layer 2 Isolation | Not available
Notes: The characteristics and features available in STATIC network mode. Note that in this network mode, the Cluster Controller is now providing the DHCP server functionality.

## Slide 11: STATIC – Logical View
Walrus
storage
Cloud
Controller
Cluster
Controller
Storage
Controller
Node
Controller
Node
Controller
Node
Controller
Node
Controller
corporate LAN
provides DHCP for
virtual machines
VM
VM
VM
Br
Notes: Here is what the network mode looks like logically. Other than the Cluster Controller providing the instances with their IP addressses, STATIC network mode operates in the same way as SYSTEM mode. Each virtual machine will use this IP address for not only communication to nodes external to the cloud, but also to other virtual machines within the cloud.
All virtual machines have direct network access using the virtual bridge created by the hypervisor in the Node Controller. There are no virtual subnets—instances appear on the physical network as if they were physical machines.
It is up to IT management to manage any network security firewalls or network address translation that might be required by the organization.

## Slide 12: STATIC Network Mode
Instance receives a single IP address at boot from the Cluster Controller’s DHCP server
  Offers administrators more control over IP address assignment
Eucalyptus administrator configures a map of MAC-to-IP addresses on Cluster Controller
  VNET_MACMAP in eucalyptus.conf
  Instances are assigned first available address pair
All instances have direct network access through the network bridge created in the Node Controller.
  Appear as physical machines on the network
IT administration’s responsibility to manage security (firewalls) or network address translation.
Notes: Each virtual machine receives a single IP address from the DHCP server. The Cluster Controller runs the dhcpd daemon. The daemon uses the Eucalyptus generated /var/run/eucalyptus/net/euca-dhcp.conf configuration file.
STATIC network mode offers the Eucalyptus administrator more control over instance IP address assignment. The administrator configures Eucalyptus with a mapping of MAC address to public IP address pairs in the /etc/eucalyptus/eucalyptus.conf file. When an instance is instantiated, an unused MAC-to-IP address pair is chosen for the instance.
Like SYSTEM mode, a bridge must be created on the Node Controllers for Eucalyptus to use. All virtual machines have direct network access using the virtual bridge created by the hypervisor in the Node Controller.

## Slide 13: STATIC – Physical Example
company network
173.205.188.130 eth0
173.205.188.131 eth0
173.205.188.132 eth0
Node Controller
Node Controller
front-end DHCP (CLC Walrus CC SC)
Notes: Here is a simple illustration of STATIC network mode configuration.
In first diagram on the left, you would need to ensure that the Eucalyptus DHCP server does not respond to any other network address requests.

## Slide 14: STATIC Network Mode Requirements
A range of IP addresses must be available for use by Eucalyptus hosts and instances.
No pre-existing DHCP server on network.
  Or does not respond to Eucalyptus instances
The Ethernet interface on the Node Controller must be configured with a bridge.
  The DHCP server must be reachable from the bridge.
Notes: The Ethernet device on the Node Controller that communicates with the Cluster Controller must be bridged.
A range of IP addresses must be available for use by Eucalyptus hosts and instances.
There must be no pre-existing DHCP server or the existing DHCP server must be configured so that it cannot respond to instances.

## Slide 15: MANAGED, MANAGED-NOVLAN Characteristics and Features
DHCP Server | Cluster Controller
Elastic IP Addresses | Available
Security Groups | Available
VM Layer 2 Isolation | MANAGED mode only
Notes: The characteristics and features available in both MANAGED and MANAGED-NOVLAN network modes.
These are the two most popular network modes for Eucalyptus deployments.
Elastic IP addresses and security groups are covered in greater detail in later modules.

## Slide 16: MANAGED(-NOVLAN) – Logical View
Walrus
storage
Cloud
Controller
Cluster
Controller
Storage
Controller
Node
Controller
Node
Controller
Node
Controller
Node
Controller
corporate LAN
provides DHCP for
virtual machines
switch
subnet boundary
corporate
DHCP
server
VM
VM
VM
Br
Notes: This is how it looks logically.
It’s okay to have a corporate DHCP server as long as it is not able to respond to address requests by the DHCP server running on the Cluster Controller.
Like STATIC and SYSTEM modes, in MANAGED-NOVLAN mode a bridge must be created on the Node Controllers for Eucalyptus to use. All virtual machines have direct network access using the virtual bridge created by the hypervisor in the Node Controller.
In MANAGED mode, a bridge does not have to be created ahead of time. In MANAGED mode, the system does use bridges, but eucalyptus will create, manage, and remove them automatically. With MANAGED mode, for each security group there is a bridge created on both Cluster Controller and Node Controller. These bridges are VLAN tagged interfaces.

## Slide 17: MANAGED(-NOVLAN) – Physical Example
company network
eth0 “public” interface
eth0
Node Controller
eth1 “private” interface
public switch
private switch
front-end DHCP (CLC Walrus CC SC)
Cluster Controller on front-end host will act as router between VMs and company network
Notes: This is a really simple physical example.

## Slide 18: IP Address Requirements
The virtual machines will use two IP address ranges. Why?
Each virtual machine is assigned two IP addresses
  A private IP address for VM-to-VM communication
  A public IP address for cloud-external communication
Cluster Controller maps private IP addresses to public IP addresses
  Using iptables nat table
Eucalyptus physical hosts also require IP addresses to communicate
NAT
CLC
CC
NC
NC
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
public IP range (example: available addresses in your company’s network)
private IP range (example: 10.1.0.0\16 )
public switch
private switch
DHCP
Notes: Remember that this is a private cloud so “public” IP addresses are more than likely IP addresses that are internal to the company but visible to users and applications outside the cloud.

## Slide 19: IP Addresses Illustration
Example IP addresses used to illustrate MANAGED(-NOVLAN) mode networking.
10.1.0.41
205.16.2.20
private IP virtual network
overlay
10.1.0.0
physical switch
VM1
10.1.0.41
NC
NC
205.16.3.11
CC
(front-end)
205.16.2.11
10.1.0.X
VM2
10.1.0.42
NC
205.16.3.12
physical host IP addresses
company IP network 205.16.2.20-39
private VM addresses
VM IP address translation
205.16.3.10

## Slide 20: Private IP Range
Private IP range for virtual machines is automatically divided into subnets by Eucalyptus
Range, number of subnets, and virtual machines per subnet configured by parameters in /etc/eucalyptus/eucalyptus.conf
Why? Subnet configuration determines:
  Maximum number of security groups* (one per subnet)
  Maximum number of instances per security group (number of addresses per subnet)
*Cloud users create firewall rules using security groups.
NC
.
.
.
virtual subnet
virtual subnet
virtual subnet
VM
VM
VM
VM
VM
VM
private IP range 10.1.0.0

## Slide 21: Private IP Address Configuration
When configuring private IP address range, be aware that:
  10 IP addresses per subnet are reserved.
    1 network number, 1 broadcast address, 8 gateway addresses
  Eucalyptus uses 4092 VLAN IDs (2-4094)
16 subnet bits = 65,536 possible addresses
VNET_MODE=“MANAGED”
VNET_SUBNET=“10.1.0.0”
VNET_NETMASK=“255.255.0.0”
VNET_ADDRSPERNET=“32”
65,536 / 32 = 2048 possible subnets
min of(4092, 2048) = 2048 actual subnets
32 ADDRSPERNET – 10 = 22 instances per subnet
eucalyptus.conf
Notes: Eucalyptus 3 supports a maximum of eight clusters and each Cluster Controller will have a gateway IP address in each subnet. For this reason eight IP addresses are reserved from each subnet that is created.
VNET_SUBNET determines the network prefix used for the virtual machines’ private IP addresses.
VNET_NETMASK determines the total address space available to for the virtual machines’ private IP addresses.
VNET_ADDRSPERNET determines how the virtual machines’ private IP address space will be subnetted by Eucalyptus. A larger number of addresses per net will result in few subnets (security groups) while a smaller number of addresses per net results in a larger number of subnets (security groups). These VNET settings must be configured identically across all Cluster Controllers in the cloud.
To prevent different Cluster Controllers from allocating the same public or private IP addresses, each Cluster Controller will broadcast a set of 'capabilities' (I have this many public IPs, this many private subnets, this networking mode, etc) up to the Cloud Controller. When it comes time to start a network or run some instances, the Cloud Controller will send a unique index down to the Cluster Controller which will use the index to select a corresponding actual network value (whether it be public IPs, private IPs, or entire security group subnet ranges). Since the Cloud Controller is the component that knows about multiple clusters, it is the one responsible for keeping those bits uniquely allocated.

## Slide 22: MANAGED-NOVLAN VM Isolation
Virtual machine isolation is managed only at the IP layer through security groups. (iptables filter table)
  A subnet is automatically used when the first instance in a security group is started.
  A subnet is released when the last instance in the security group is terminated.
  Instance in one subnet could network sniff instance in another subnet if they share the same LAN and switch is promiscuous.
10.1.1.1
10.1.1.2
10.1.2.2
10.1.2.1
Security Group A
IP subnet 1
LAN
Security Group B
IP subnet 2
firewall rules
firewall rules
Notes: Virtual machine isolation is provided by IP subnets only. Virtual machines share the same LAN and therefore virtual machines in one subnet can potentially use a packet capture utility to capture network packets from another subnet. If that is a concern, then you would need to configure MANAGED network mode.
A given subnet can be used by different security groups at different times.

## Slide 23: MANAGED VM Isolation
Virtual machine isolation is managed at the IP layer through security groups (iptables filter table) and VLANs (one security group per VLAN)
  A VLAN is automatically created when the first instance in a security group is started.
  A VLAN is removed when the last instance in the security group is terminated.
  An instance in one virtual subnet cannot network sniff an instance in another virtual subnet
10.1.1.1
10.1.1.2
10.1.2.2
10.1.2.1
Security Group A
IP subnet 1
VLAN 1
Security Group B
IP subnet 2
firewall rules
firewall rules
VLAN 2
Notes: VLAN assignment is based on an available number when the first instance in a new security group starts up. A given VLAN ID might be used by different security groups at different times.
When Eucalyptus is configured in MANAGED network mode it will assign a VLAN ID to each security group when the first instance in that security group is launched. The VLAN ID will remain in use until the last instance in the security group is deleted.
Eucalyptus it is able to use VLAN IDs 2-4094 by default. The maximum ID number depends on two factors. First, the highest ID number will depend on the maximum number of security groups your cloud configuration supports. You can determine this number by running the commands euca-describe-properties | grep cluster.maxnetworktag and euca-describe-properties | grep cluster.minnetworktag.
Second, the range of available IDs may be further changed by setting the system properties euca-modify-property -p cloud.network.global_max_network_tag=<max_vlan_tag> and euca-modify-property -p cloud.network.global_min_network_tag=<min_vlan_tag>.

## Slide 24: VLAN-Clean Testing
To test whether the network switches are VLAN-clean choose:
  Two private IP addresses
  One VLAN ID
  CC and NC network interfaces
On the Cluster Controller:
  vconfig add eth1 10
  ifconfig eth1.10 10.1.1.1 up
On the Node Controller:
  vconfig add eth0 10
  ifconfig eth0.10 10.1.1.2 up
From each host, ping the IP address of the other host.
CC
NC
NC
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
other VLANS ok here
Must be VLAN clean here
public switch
private switch
Notes: In MANAGED network mode the Cloud Controller will automatically make sure that each security group (subnet) is assigned a unique VLAN ID. This means that Ethernet packets flowing between the Cluster Controller and the Node Controllers will be VLAN tagged. This creates two requirements for the network switches between the Cluster Controller and Node Controllers. First, they must be able to read and forward VLAN-tagged packets. Second, theses network switches must not be already using any VLAN IDs that Eucalyptus will be using. Network switches that can read and forward VLAN-tagged packets and do not have an VLAN ID conflicts are said to be ‘VLAN clean’ from a Eucalyptus perspective.
After testing as in the example above, remove the virtual interfaces use the syntax vconfig rem eth1.10 and vconfig rem eth0.10.

## Slide 25: Routing – Two Clusters/Single Subnet
Security Group: A
Network: 10.1.0.32
VM IPs: 10.1.0.41-62
Broadcast: 10.1.0.63
GW IP: 10.1.0.33
Security Group: A
Network: 10.1.0.32
VM IPs: 10.1.0.41-62
Broadcast: 10.1.0.63
GW IP: 10.1.0.34
CC1
CC2
physical switch (205.16.3.0)
VM1
VM2
NC
NC
NC
NC
private 10.1.0.0
network
hostA
eucalyptus.conf
VNET_SUBNET=“10.1.0.0”
VNET_NETMASK=“255.255.0.0”
VNET_ADDRSPERNET=“32”
subnet ranges VLAN ID
10.1.0.0 – 10.1.0.31 2
10.1.0.32 – 10.1.0.63 3
10.1.0.64 – 10.1.0.95 4
packet routing
VM1 to VM2 direct route
VM1 to hostA via GW 10.1.0.33
VM2 to hostA via GW 10.1.0.34
company network 205.16.2.0
10.1.0.41
10.1.0.42
Notes: In this example, each subnet has 32 possible addresses. However, ten addresses in each subnet cannot be assigned to virtual machines. In each subnet one IP address is used for the broadcast address, one address is used for the network number, and eight addresses are used as gateway IP addresses for routing IP packets from virtual machines to nodes outside of the cloud.
Why are eight IP addresses in each subnet reserved as gateway IP addresses? Because each subnet is also a security group and a security group can span up to eight Cluster Controllers. Each Cluster Controller requires its own gateway IP address for each security group.
In the example above, security group A contains virtual machines on two Cluster Controllers so two of the possible eight gateway IP addresses that subnet are actually in use. VM1 communicates directly with VM2 across the physical switch using their private IP addresses. However, VM1 and VM2 must use the gateway IP addresses on their Cluster Controllers to communicate with hostA.
The Cloud Controller chooses a random VLAN ID and IP addresses range for the next security group. VLAN IDs 0 and 1 are not used as they reserved.
The Cloud Controller chooses an instance IP address at random from the range of available IP addresses in the subnet.

## Slide 26: Routing – Two Clusters/Two Subnets
Security Group: A
Network: 10.1.0.32
VM IPs: 10.1.0.41-62
Broadcast: 10.1.0.63
GW IP: 10.1.0.33
Security Group: A
Network: 10.1.0.32
VM IPs: 10.1.0.41-62
Broadcast: 10.1.0.63
GW IP: 10.1.0.34
CC1
CC2
physical switch (205.16.3.0)
VM1
VM2
NC
NC
NC
NC
hostA
eucalyptus.conf
VNET_SUBNET=“10.1.0.0”
VNET_NETMASK=“255.255.0.0”
VNET_ADDRSPERNET=“32”
subnet ranges VLAN ID
10.1.0.0 – 10.1.0.31 2
10.1.0.32 – 10.1.0.63 3
10.1.0.64 – 10.1.0.95 4
packet routing
VM1 to VM2 through tunnel
VM1 to hostA via GW 10.1.0.33
VM2 to hostA via GW 10.1.0.34
company network 205.16.2.0
10.1.0.41
10.1.0.42
physical switch (205.16.4.0)
IP tunnel
private 10.1.0.0
network
Notes: The change in this example is that the two Cluster Controllers are no longer on the same subnet. In this example, Eucalyptus must use the vtun interfaces on the Cluster Controllers to create an IP tunnel between the two Cluster Controllers. The vtun interface depends on the two Cluster Controllers having a physical network route to one another. The IP tunnel is created across this route. The IP tunnel creates the illusion that VM1 and VM2 in security group A are on the same subnet. From the perspective of virtual machines in a common security group, they can broadcast ARP packets, receive ARP responses, and have a direct route between themselves.
If the routing table on the Cluster Controllers is watched, you would see tunnels being created and destroyed as virtual machines in the same security group are being launched and terminated on the two Cluster Controllers.
Tunnel interfaces are a point of congestion and latency and therefore this configuration is not a Eucalyptus recommended configuration.

## Slide 27: MANAGED(-NOVLAN) Network Mode Requirements
A range of public IP addresses must be available for instances.
A range of private IP addresses must be available for the instances.
A set of physical IP addresses must be available for the Eucalyptus components.
The Cluster Controller firewall must be compatible with the dynamic changes performed by Eucalyptus.
The network must be VLAN-clean (MANAGED mode only).
Notes: There is an available range of IP addresses to be used for the virtual subnets that do not interfere with the physical network. These IP addresses are often selected from the private IP ranges: 10.0.0.0-10.255.255.255, 172.16.0.0-172.31.255.255, and 192.168.0.0-192.168.255.255.
The supported versions of Linux use the iptables firewally which is compatible with and can be controlled by Eucalyptus software running on the Cluster Controllers. Note that Eucalyptus software will flush the ‘nat’ and ‘filter’ tables in iptables at start up.
A range of IP addresses must be available for use by the physical Eucalyptus hosts and also available for the public IP addresses of the instances.
Part of the network infrastructure must also be VLAN-clean. There is more detail about VLAN-clean on the next slide.

## Slide 28: Network Modes Review
 | SYSTEM | STATIC | MANAGED-NOVLAN | MANAGED
DHCP Server | Corporate | Yes | Yes | Yes
Elastic IP Addresses | No | No | Yes | Yes
Security Groups | No | No | Yes | Yes
VM Layer 2 Isolation | No | No | No | Yes
Notes: Side-by-side review of all network modes and their supported features.

## Slide 29: Choose a Network Mode
elastic IPs,
security groups
layer 2 VM isolation
corporate DHCP server
corporate DHCP server
VLAN clean
MANAGED
decide on features
MANAGED NOVLAN
SYSTEM
STATIC
not possible
yes
yes
yes
yes
yes
no
no
no
no
no

## Slide 30: eucalyptus.conf
Central configuration file
Where network mode configuration takes place
  On Cluster Controller and Node Controller
Also defines settings for other cloud components
Any change to the network configuration requires a Cluster Controller clean restart.
  Terminate all instances first
  Run service eucalyptus-cc cleanrestart
    Flushes all network configuration

## Slide 31: Cluster Controller Network Parameters
MANAGED | MANAGED-NOVLAN | STATIC | SYSTEM
VNET_MODE | VNET_MODE | VNET_MODE | VNET_MODE
VNET_PUBINTERFACE | VNET_PUBINTERFACE | VNET_PRIVINTERFACE | 
VNET_PRIVINTERFACE | VNET_PRIVINTERFACE | VNET_DHCPDAEMON | 
VNET_DHCPDAEMON | VNET_DHCPDAEMON | #VNET_DHCPUSER | 
#VNET_DHCPUSER | #VNET_DHCPUSER | VNET_SUBNET | 
VNET_SUBNET | VNET_SUBNET | VNET_NETMASK | 
VNET_NETMASK | VNET_NETMASK | VNET_BROADCAST | 
VNET_DNS | VNET_DNS | VNET_ROUTER | 
VNET_ADDRSPERNET | VNET_ADDRSPERNET | VNET_DNS | 
VNET_PUBLICIPS | VNET_PUBLICIPS | VNET_MACMAP | 
#VNET_LOCALIP | #VNET_LOCALIP |  | 
Notes: These are network parameters that must be checked and possibly set in the eucalyptus.conf file for each network mode on Cluster Controller.
If you are running multiple clusters, you may wish to explicitly specify the IP address that the Cluster Controller used to register with the Cloud Controller. You may set the variable VNET_LOCALIP="<ip_of_cluster_controller>"
in the configuration file for each of the Cluster Controllers.
Parameters prefaced with a # symbol are optional and may only be set in specific configurations.

## Slide 32: Node Controller Network Parameters
MANAGED | MANAGED-NOVLAN | STATIC | SYSTEM
VNET_MODE | VNET_MODE | VNET_MODE | VNET_MODE
VNET_PUBINTERFACE | VNET_PUBINTERFACE | VNET_BRIDGE | VNET_BRIDGE
VNET_PRIVINTERFACE | VNET_PRIVINTERFACE |  | 
VNET_BRIDGE | VNET_BRIDGE |  | 
Notes: These are the network parameters that must be set in eucalyptus.conf on the Node Controller host(s).

## Slide 33: Summary
Four network modes are available.
  SYSTEM, STATIC, MANAGED-NOVLAN, MANAGED
Choice depends on the features required or desired along with the level of control over the underlying physical network.
SYSTEM mode is simplest, but has the fewest features.
MANAGED mode is the most secure and has the most features.
Network mode is configured in the eucalyptus.conf file.

## Slide 34
End of Module